PLU Building Safety Inspection Checklist

Building/Department(s): _______________________________ Date:_________ _________Time:______________

Inspector(s): _____________________________ ________Building Representative: ________________________

| Checklist Items | Yes | No | NA |
| --- | --- | --- | --- |
| A. General – All Areas |
| 1. Are all ceiling tiles in place and in good condition? |  |  |  |
| 2. Is all furniture in good/stable condition and properly adjusted? |  |  |  |
| 3. Are wall-mounted bookcases free of excessive materials on top and not overloaded? Chemicals & heavy items should not be stored above head height (6 ft) |  |  |  |
| 4. Are all walking or working surfaces free of tripping/slipping hazards? |  |  |  |
| 5. Are emergency phone numbers and procedures posted at or near telephones? |  |  |  |
| 6. Are all fans equipped with a blade guard with openings no greater than ½ inch? |  |  |  |
| 7. Is consumption of food, beverage, etc. prohibited where required? |  |  |  |
| B. General – Shops |
| 1. Are machine and belt guards in place and in good condition? |  |  |  |
| 2. Is pedestal machinery securely anchored to the floor? |  |  |  |
| 3. Is equipment properly maintained and adjusted to prevent personal injury and equipment damage? |  |  |  |
| 4. Is all piping appropriately identified as to contents/direction of flow? |  |  |  |
| 5. Are hot pipes and surfaces guarded against contact and clearly marked “HOT”? |  |  |  |
| 6. Are areas requiring use of protective equipment (e.g. Eye Protection Required) adequately posted with warning signs and enforced? |  |  |  |
| 7. Is damaged/malfunctioning equipment tagged “Out of Service”? |  |  |  |
| C. General – Labs/Studios |
| 1. Are working surfaces clear and organized? |  |  |  |
| 2. Are working surfaces made from non-porous & chemical resistant materials? |  |  |  |
| 3. Are phones accessible and emergency numbers posted? |  |  |  |
| 4. Are hazards signs and contact names for the lab/studio posted on the outside of the lab? |  |  |  |
| 5. Are areas requiring use of personal protective equipment adequately posted with warning signs and enforced? |  |  |  |
| 6. Is safety instruction part of each lab or class? |  |  |  |
| 7. Are ventilation hoods NOT used to store chemicals? |  |  |  |
| D. Exits/Corridors |
| 1. Are all corridors unobstructed? |  |  |  |
| 2. Are all exit doors unobstructed? |  |  |  |
| 3. Are exit signs posted and properly illuminated to clearly indicate exits? |  |  |  |
| 4. Are all exit doors able to be opened from the inside without special knowledge/keys? |  |  |  |
| 5. Are exit doors free of slide bolts or locks? |  |  |  |
| Items left unmarked were not observed. E. Electrical |
| 1. Is there at least three (3) feet of clearance in front of electrical panels? |  |  |  |
| 2. Are electric hand tools properly grounded/double insulated? |  |  |  |
| 3. Is the area free of extension cords? (Surge protectors - not power strips - are allowed) |  |  |  |
| 4. Is all electrical equipment plugged directly into the wall outlets? |  |  |  |
| 5. Are all cords/plugs free from damage or deterioration? |  |  |  |
| 6. Are switches and circuit breakers properly identified as to the service they are in and to what they control? |  |  |  |
| 7. Are circuit breaker panels free of combustible materials? |  |  |  |
| 8. Are cover plates in place on junction boxes to eliminate exposed wiring? |  |  |  |
| 9. Are “Warning High Voltage” signs installed on high voltage enclosures for systems rated 600V or over? |  |  |  |
| 10. Is all electrical, including light fixtures, protected from physical damage by enclosure/guards? |  |  |  |
| F. Emergency Equipment |
| 1. Is emergency equipment (alarm pull boxes, eyewashes, showers, etc.) accessible and not blocked by equipment? |  |  |  |
| 2. Are emergency eyewashes/showers provided in the required chemical areas? |  |  |  |
| 3. Are eyewash/showers flushed weekly and inspected annually? |  |  |  |
| 4. Is all emergency equipment in good condition? |  |  |  |
| 5. Are spill kits accessible and fully stocked? |  |  |  |
| G. Storage - General |
| 1. Is good housekeeping practiced in work area? |  |  |  |
| 2. Is storage adequately supported/stable to avoid tipping/falling? |  |  |  |
| 3. Is there at least two (2) feet clearance between stacked materials and ceiling light? |  |  |  |
| H. Storage – Fire Protection |
| 1. Is the storage of combustibles in the work area held to a minimum to avoid a fire hazard? |  |  |  |
| 2. Is clearance of at least 18 inches maintained around fire sprinkler heads and 2 feet below ceiling height? |  |  |  |
| 3. Are flammable/combustible liquids in excess of one day’s operational supply kept in approved flammable materials storage (FMS) cabinets? |  |  |  |
| 4. Are all FMS cabinets free of combustible materials (cardboard, paper, plastic, etc.) |  |  |  |
| 5. Are all flammable containers properly closed/covered to control vapors? |  |  |  |
| 6. Are combustible items at least 18 inches from heat source? |  |  |  |
| 7. Are all refrigerators used for storage of flammable/combustible liquids/materials approved and explosion proof? |  |  |  |
| 8. Are flammable/combustible liquids returned to approved flammable liquid storage cabinets at the end of the workday? |  |  |  |
| 9. Are sprinkler valves unobstructed? |  |  |  |
| I. Storage – Compressed Gas Cylinders |
| 1. Are all cylinders properly secured with straps or chains to prevent tipping/falling? |  |  |  |
| 2. Are protective valve caps in place when cylinder is not in use? |  |  |  |
| 3. Are empty and full cylinders stored separately? |  |  |  |
| 4. Are only chemically compatible cylinders stored together? |  |  |  |
| 5. Are cylinder contents adequately labeled and easily seen? |  |  |  |
| 6. Is the correct regulator being used for the cylinder service? |  |  |  |
| 7. Are highly toxic gases stored in vented gas cabinets? |  |  |  |
| J. Personal Protective Equipment (PPE) |
| 1. Has a job hazard assessment been completed and signed by EHS? |  |  |  |
| 2. Is the requirement to use protective equipment enforced? |  |  |  |
| 3. Is the proper PPE worn? |  |  |  |
| 4. When not in use, is PPE properly maintained/stored? |  |  |  |
| 5. Is PPE readily available for all personnel including visitors to the area? |  |  |  |
| 6. Are all employees using respiratory protection properly trained and authorized by EHS? |  |  |  |
| K. Hazardous Materials |
| 1. Are hazardous materials labeled with the name of the material and the primary hazard, e.g. flammable, toxic |  |  |  |
| 2. Materials Safety Data Sheets are available for all hazardous materials present. MSDS are current. |  |  |  |
| 3. Are hazardous wastes labeled as such? |  |  |  |
| 4. Are hazardous materials stored properly, e.g. compatibles, flammable cabinets, toxics locked? |  |  |  |
| 5. Do containers look undamaged? |  |  |  |
| 6. Are there spills or leaks? |  |  |  |
| L. Railing/Elevated Work Areas |
| 1. Are drain openings, pits in the floor, or walking surfaces guarded to prevent tripping/slipping? |  |  |  |
| 2. Are toeboards in place on elevated platforms to prevent objects from falling off the platform? |  |  |  |
| 3. Are standard guardrails provided on elevated platforms? |  |  |  |
| 4. Are handrails provided and in good condition on stairways? |  |  |  |
| 5. Are there provisions for safe access to elevated machinery/equipment? |  |  |  |
| M. Ladders |
| 1. Are portable ladders in good repair and safe to use? |  |  |  |
| 2. Are mobile ladder stands in good condition? |  |  |  |
| N. Forklifts |  |  |  |
| 1. Are defective forklifts taken out of service and tagged “Do Not Use”? |  |  |  |
| 2. Are forklift inspection forms current and maintained in a file? |  |  |  |
| 3. Are load limits clearly posted in the area? |  |  |  |
| 4. Are forklift operating rules clearly posted in the area? |  |  |  |
| 5. Are all operators trained and authorized? |  |  |  |
| O. Fire Protection |
| 1. Are emergency evacuation plans posted? |  |  |  |
| 2. Are all self-closing doors operational (No doorstops)? |  |  |  |
| 3. Are walls and floors free of holes/penetrations? |  |  |  |
| 4. Are no smoking regulations clearly posted and being followed in “No Smoking” areas? |  |  |  |
| 5. Are fire extinguishers and signs clearly visible? |  |  |  |
| 6. Is access to fire extinguishers clear and unobstructed? |  |  |  |
| 7. Are all extinguishers in place and properly inspected (monthly) and maintained (annually)? |  |  |  |
| 8. Is the building number or address posted? |  |  |  |
| P. Training |
| 1. Have personnel been trained in the use of personal protective equipment? |  |  |  |
| 2. Are all employees trained in hazardous substances safety? |  |  |  |
| 3. Have personnel working in high noise areas been trained in hearing conservation? |  |  |  |
| 4. Have employees who use respirators been trained, fit tested, and received the required health monitoring examination? |  |  |  |
| 5. Have employees been trained in emergency procedures? |  |  |  |
| 6. Other training: |  |  |  |
| Q. Ergonomics |
| 1. Are desk chairs equipped with seat and back height and tilt adjustments? |  |  |  |
| 2. Do you see anyone working in an awkward position? |  |  |  |
| 3. Do employees have tools to assist in lifting and moving heavy or awkward materials? |  |  |  |
| 4. Are employees using proper lifting techniques? |  |  |  |
| R. Grounds |
| 1. Are walking or working surfaces free of tripping/slipping hazards? |  |  |  |
| 2. Is vegetation maintained to provide clear visibility, clearance around light fixtures, and safe pathways? |  |  |  |
| S. Computer Rooms |
| 1. Are combustibles stored in approved, enclosed metal cabinets? |  |  |  |
| 2. Is combustible waste, e.g. trash containers, cardboard boxes, etc., removed from the room daily or more often as needed? |  |  |  |
| 3. Is the computer room free of flammable/combustible liquids? |  |  |  |
| 4. Are computer tapes stored in approved, enclosed metal cabinets? |  |  |  |
| 5. Is the raised floor free of unsealed cable holes? |  |  |  |
| 6. Is the access to fire suppression and alarm systems unobstructed? |  |  |  |
| 7. Are floor tile pullers available and mounted? |  |  |  |
| 8. Are doors to the peripheral rooms closed? |  |  |  |
| 9. Is paper stored in computer room limited to a one-day supply? |  |  |  |
| 10. Is the room free of repair shop operations? |  |  |  |
| 11. Is the room free of soldering irons? |  |  |  |
| 12. Is the room free of coffee makers, electric floor/space heaters, etc.? |  |  |  |
| T. Lockout / Tagout |  |  |  |
| 1. Are LO/TO procedures followed? |  |  |  |
| U. Confined Spaces |  |  |  |
| 1. Are Confined Spaces procedures followed? |  |  |  |

Explanation/Comments on all No Answers – Note Item identification from checklist, e.g. A.1, and Location